## Slide 1: Evaluation of Stochastic Computing for Efficient Deep Neural Network Inference
Master Thesis - Javier Ferrer Ortega

## Slide 2: AGENDA
Theoretical Background
SC DNN Framework Implementation & GPU Acceleration
Results
Conclusions

## Slide 3: Theoretical Background

## Slide 4: Stochastic Computing?
Alternative to traditional binary computation.
Treats computed numbers as probabilities 𝑝𝑋, refered as stochastic numbers -> represented by bitstreams of random 1s and 0s.
Neither the length nor the structure of a bitstream needs to be fixed, so:
[1,0,0,0]
[0,1,0,0]
[0,1,0,0,0,1,0,0]
Binary Computation
stochastic number
𝑝𝑋 = 0.25
0.012​
Decimal number
x = 0.25
to binary
Arithmetic operations are realized by means of single logic gates like AND, OR…
Arithmetic operations:
  Addition:
    Full adder
    Ripple-carry adder
    Carry-lookahead adder
  Multiplication:
    Booth's algorithm multiplier

## Slide 5: Stochastic number generation & convertion to binary:
Binary to stochastic. (b) Stochastic to binary.
Taken from [1].
A comparison of stochastic numerical formats
Table 1. Taken from [2].
If bipolar: x = 0.5 (1 + 0.25) = 0.625 -> [1, 1, 0, 1] -> px = ¾
If bipolar:
bin. no. = (2*px - 1)
Stochastic
Bitstream
[0,0,0,1]
Stochastic
Bitstream
[0,0,0,1]
px = N1 / N = 1/ 4
N1: total no. of ones
N: bitstream length
range [0 , 1] [-1 , 1]
0.25
[0.34, 0.56, 0.78, 0.11]

## Slide 6
Stochastic Computing Operations:
(d)
SC multiplier: AND gate – Unipolar bitstreams
SC multiplier: XNOR gate – Bipolar bitstreams
(c) SC adder: MUX
(d) SC adder: OR gate
pA + pB = pQ
pA + pB = pQ

## Slide 7: Benefits
SC allows the operation of arithmetic functions with very few logic gates in hardware designs:
Addition: MUX / OR gate
Multiplication: AND / XNOR gate
Small component size -> low power applications
High error tolerance -> resilient to bit flippings (e.g. found in bit-flipping attacks [3] or radiation-induced errors [4]).

## Slide 8: Benefits vs Drawbacks
SC allows the operation of arithmetic functions with very few logic gates in hardware designs:
Addition: MUX / OR gate
Multiplication: AND / XNOR gate
Small component size -> low power applications
High error tolerance -> resilient to bit flippings (e.g. found in bit-flipping attacks [3] or radiation-induced errors [4]).
Longer computation times that lead to->
higher energy consumption costs (energy = power × time)
Low precision applications (e.g. image processing, DNNs computation) ->
Only 4 stochastic bits needed to represent 0.25 -> (1,0,0,0) but to represent 0.5625 accurately, the stochastic bitstream must be longer -> (0,1,0,1,0,1,0,1,0,1,0,1,0,1,1,1): 16 bits.

## Slide 9: SC DNN Framework
Why? - Motivation: To compare different SC DCNNs and evaluate the requirements needed to achieve effective inference using Stochastic Computing.
How? – Framework Architecture:
  Stochastic Tensor Generator
  SC 2D convolution
  SC Fully Connected Layer
However…

## Slide 10: SC DNN Framework: SC 2D convolution & SC Fully connected layers
A Stochastic Computing extension to PyTorch’s DNN functions, in CPU:
Chart: Execution Time (mins) 1 layer of the SC Conv2d in CPU
| 10x10 | 50x50 | 100x100 | 250x250 | 500x500 | 1000x1000
cpu | 0.007445 | 0.024822 | 0.10731 | 0.64879 | 2.6076 | 10.6451
Chart: Execution Time (mins) 1 layer of the SC FC Layer in CPU
| 84/10 | 120/84 | 400/120 | 1024/400 | 2048/500 | 3072/600
 | 0.0010817 | 0.012025 | 0.057558 | 0.50178 | 1.3678 | 2.6605

## Slide 11: GPU Acceleration

## Slide 12: Objective: Reduce SC Conv2d and SC FC Layer functions’ CPU time complexities “O(n)” with GPUs’ multi-threaded data-parallelism
Stochastic Tensor Generator CPU O(n) time complexity:
FLOPs:
Table 2. A comparison of 2D convolutions computational complexity. Taken from [3].
Fully Parallelized
Stochastic Bitstream

## Slide 13: Objective: Reduce SC Conv2d and SC FC Layer functions’ CPU time complexities “O(n)” with GPUs’ multi-threaded data-parallelism
Stochastic Tensor Generator CPU O(n) time complexity:
FLOPs:
SC 2D Convolution CPU O(n) time complexity:
GPU O(n):
SC Fully Connected Layer CPU O(n) time complexity:
GPU O(n):
Fully Parallelized
Stochastic Bitstream

## Slide 14
HARDWARE
Memory Hierarchy
Taken from [5].
CUDA kernel execution model
Taken from [4].

## Slide 15: CUDA STREAMS
Taken from [6].

## Slide 16: SC CNN CUDA model
(‘biases’)
Taken from [6].
CUDA STREAMS

## Slide 17: Stochastic Tensor Generator kernel - parallel approach

## Slide 18: SC 2D Convolution kernel - parallel approach
A
B
C
0,1,0,1…
1,0,1,0…
D
E
F
0,1,0,1…
1,1,1,1…
G
H
I
0,0,0,0…
1,1,1,1…
0,0,0,0..
1,1,1,1…
0,1,0,1…
0,1,0,0…
0,0,0,1…
0,0,0,0…
0,0,1,0…
1,0,1,1…
0,1,0,1…
0,0,0,1…
a
b
c
d
e
f
g
h
i
0,1,0..
0,1,0..
0,1,1..
0,0,1..
0,0,1..
1,1,1..
0,0,0..
1,0,1..
5 x 5
3 x 3
3 x 3
2D Image
2D Convolution
Filter
2D Convolution
Output
Thread id_0
AND/XNOR
Accum_
Output [0] [0]

## Slide 19: SC Fully Connected Layer kernel - parallel approach
Thread id_0
1,0,1..
1,1,1..
1,1,0..
0,1,0..
0,1,1..
weights[0][0]
weights[0][1]
weights[0][2]
weights[0][3]
weights[0][4]
Bias_1
1,1,0..
1,1,1..
1,1,0..
0,1,1..
0,1,0..
1,1,1..
A
B
C
D
E
AND/XNOR
AND/XNOR
AND/XNOR
AND/XNOR
AND/XNOR
Out1
Out2
Out3
Accum_
Accum_
Accum_
Accum_
Accum_
Input Neurons
Output Neurons
Output [0]

## Slide 20: Results

## Slide 21: End-to-end execution time [ms] of 1 single layer of a SC 2D Convolution & 1 SC Fully Connected Layer: CPU vs GPU
*Used device: NVIDIA V100
Gain = x500 (≈2.5 orders of magnitude)
Gain = x150 (≈2 orders of magnitude)

## Slide 22: Percentage % of correctly inferred images with SC LeNet-5 per bitstream length (1000 images in total from fashionMNIST dataset)
Chart: Bitstream length
| Unipolars 512 | Unipolars 256 | Bipolars 512
 | 98.2 | 96.5 | 52.4
LeNet-5 architecture: 2 convs, 3 fcls
Taken from [7].
*Used device: NVIDIA V100

## Slide 23: Mean Absolute Error per layer in SC LeNet-5 (average MAE after 100 inferred images of the Sneaker class)
Chart: SC LeNet-5 layers
| 1rst Conv2d | 2nd Conv2d | 1rst FCLayer | 2nd FCLayer | 3rd FCLayer
Bipolars Clipped to [-1,1] | 0.8072 | 0.6907 | 0.2072 | 0.2878 | 3.4213
Unipolars Clipped to [0,1] | 0.0593 | 0.098 | 0.0445 | 0.0419 | 0.1909
Chart: SC LeNet-5 layers
| 1rst Conv2d | 2nd Conv2d | 1rst FCLayer | 2nd FCLayer | 3rd FCLayer
Bipolars Clipped to [-1,1] | 0.3571 | 0.3789 | 0.2914 | 0.4472 | 0.1068
Unipolars Clipped to [0,1] | 0.9958 | 0.9922 | 0.9939 | 0.9952 | 0.9978
Cosine Similarity per layer in SC LeNet-5
(average similarity after 100 inferred images of the Sneaker class)

## Slide 24: Execution time per layer in SC LeNet-5
SC LeNet-5 throughput in frames per minute
Chart: SC LeNet-5 layers
| 1rst Conv2d | 2nd Conv2d | 1rst FCLayer | 2nd FCLayer | 3rd FCLayer
Unipolars normalised to [0,1] | 0.80591 | 2.6181 | 3.171 | 1.045 | 0.09757
Bipolars clipped to [-1,1] | 1.0382 | 3.3492 | 3.8468 | 1.2732 | 0.11778
Unipolars clipped to [0,1] | 0.81269 | 2.623 | 3.1815 | 1.0491 | 0.097859
Chart: Bitstream Length
| 1280 | 1024 | 768 | 512 | 256
Unipolars clipped to [0,1] | 3.3123 | 4.1277 | 5.4934 | 7.4671 | 16.2911
Bipolars clipped to [-1,1] | 2.5246 | 3.1639 | 4.1881 | 6.1332 | 12.0647
*Used device: NVIDIA V100

## Slide 25: Percentage % of correctly inferred images with SC VGG9 per bitstream length (300 images in total from CIFAR-10 dataset)
Chart: Bitstream length
| Unipolars 1024 | Unipolars 512 | Unipolars 256 | Bipolars 1024
 | 98.68 | 94.3 | 91 | 68.34
VGG9 architecture: 6 convs, 3 fcls
Taken from [8].
*Used device: NVIDIA A100

## Slide 26
Chart: Average inference time of a single image with SC VGG9
| Unipolars 1024 | Unipolars 512 | Unipolars 256 | Bipolars 1024
 | 2.6996 | 1.3534 | 0.69103 | 3.6373
*Used device: NVIDIA A100

## Slide 27
Chart: Average inference execution time of 300 images with SC VGG9 per RNG
| •MerseneTwster | •PCG | •XorShift* | •LFSR
 | 697.953 | 713.051 | 701.103 | 687.823
*bitstream length = 512
*bitstream length = 512
*Used device: NVIDIA A100

## Slide 28: CONCLUSIONS
Unipolar functions are more precise than bipolars because zeros are actually zeros and not approximations.
In addition, shorter stochastic unipolar bitstreams are able to represent probabilities with more decimals, unlike bipolar numbers.
Finally, unipolar functions can compute more FLOPs in the GPU implementation because it is possible to skip multiplications by 0 (accumulator does not need to be increased).
Extra observation: 16 bit LFSR be the fastest RNG but also the less precise compared to other 3 RNGs, whereas XorShift* was the RNG with less MAE and highest % of correctly inferred images.

## Slide 29
A. Alaghi and J. P. Hayes. Survey of stochastic computing. ACM Trans. Embed. Comput. Syst., 12, May 2013.
Vincent C. Gaudet Warren J. Gross. Stochastic Computing: Techniques and Applications. Springer Nature Switzerland AG, 1. edition, 2019.
Wei, T., Tian, Y. and Chen, C.W., 2020. Rethinking convolution: towards an optimal efficiency.
NVIDIA Corporation. CUDA C++ Programming Guide. NVIDIA Corporation, 2024.
Jason Sanders, Edward Kandrot, and Jack J. Dongarra. Cuda by example: An introduction to general-purpose GPU programming. Addison-Wesley/Pearson Education, 2015.
Shane Cook. CUDA Programming: A Developer’s Guide to Parallel Computing with GPUs. Morgan Kaufmann Publishers Inc., San Francisco, CA, USA, 1st edition, 2012.
https://medium.com/@pechyonkin/key-deep-learning-architectures-lenet-5-6fc3c59e6f4
Chandran, Pravin & Bhat, Raghavendra & Chakravarthi, Avinash & Chandar, Srikanth. 2021. Weight Divergence Driven Divide-and-Conquer Approach for Optimal Federated Learning from non-IID Data. 10.48550/arXiv.2106.14503.
REFERENCES